## Slide 1: Retrieving river ice parameters for ice jam prediction via MODIS on the lower Susquehanna River
NOAA/NESDIS CORP Science Symposium
10th September 2014 @ CCNY, CUNY
Simon Kraatz, PhD. Student
Advisors: Dr. N. Devineni, Dr. R. Khanbilvardi

## Slide 2: Organization
Introduction
Remote sensing of river ice
Retrieval approach
Results
Conclusion

## Slide 3: What’s an ice jam?
An ice jam is …
“… a stationary accumulation of ice or frazil that restricts flow”
- IAHR
Chenango River @ Chenango Bridge, NY.
March 4, 2014. Source: www.weather.gov

## Slide 4: Impacts
Damages infrastructure via
  Flooding
  Moving debris
Jams can go from benign to serious over short time scales
Difficult to predict which jams are problematic
March 4, 2014. Source: www.weather.gov

## Slide 5: Overview
Model for ice jam prediction
  Statistical model (GLM, MCMC …)
  Satellite river ice observation
  Automated algorithm, daily
  Prediction
Needs
  Long time series
  Frequent observations
  Appropriate spatial resolution for target region (≤500 m)
  Open data access

## Slide 6: Possible input parameters
Dynamic
  Discharge
  Temperature
  Ice presence
    Quantity (NDSI if CF)
    Age
    Thickness
Static
  River sinuosity
  Slope changes
  Constrictions and obstructions

## Slide 7: MODIS
MODIS
  Moderate spatial resolution
    Up to 250 m, (2 bands)
  Revisit time ~ 1 day
  Open access
  Long time record
    Terra since 2000
    Aqua since 2002
  Poor at seeing through weather
  MOD29 masks land and inland water bodies at 1 km
Band | Range nm
1 | 620-670
2 | 841-876
3 | 459-479
4 | 545-565
5 | 1230-1250
6 | 1628-1652
7 | 2105-2155
MODIS solar channels. Source: Vermote et al. (2011).

## Slide 8: CRIOS (Terra)
CRIOS
  Spatial resolution of 250 m
    bands (1), (2)
  Data 2003-2012 (Nov-Mar)
    Start and end date varies year to year
  Susquehanna River
  Classified
Source: Chaouch et al. , 2012.

## Slide 9: CRIOS analysis (Jan-Mar, 2003-2012)
Results
  Overall cloud fraction (CF): 0.67
  Low CF, ~every 4th day
  Little ice detected when CF > 0.2
30 km
Chart: Winter day (63/yr)
Chart: Cloud fraction
| 0.2 | 0.4 | 0.6 | 0.8 | 1
Frequency | 170 | 17 | 27 | 38 | 377
Statistics | 
Mean | 0.67
Median | 0.97
Mode | 1.00
Chart: Cloud fraction

## Slide 10: River ice test (1/25/14, @ 500 m)
MYD09A1, tc (143)
Ice jam @ Marietta, 1/23/2014
R (5, 1240 nm) – SNW/CLD
G (4, 550 nm) – ICE/SNW/CLD
B (7, 2130 nm) – CLD
MYD09A1, fc (211)
MYD09A1, fc (511)
MYD09A1, fc (547)
Susquehanna River at Marietta, PA, 02/03/14.
Source: CRREL IJDB.
Band | Range nm
1 | 620-670
2 | 841-876
3 | 459-479
4 | 545-565
5 | 1230-1250
6 | 1628-1652
7 | 2105-2155
MODIS solar channels. Source: Vermote et al. (2011).

## Slide 11: Multispectral river ice detection
Source: USGS PP-1386-A. (Ch. A-2, Fig. 77).

## Slide 12: Data processing and visualization
Raw data (each band)
  Subset
  NaN’s
  Offset and scale
    Data ranges from -0.01 to 1.60, used for computation
Optional steps
  Scale each band from 0 to 255
    Resulting images can be misleading
  Cloud mask (NN 1 km -> 500 m)
  Output to GE (GeoTIFF/KML)
  Make river mask
Raw data, Aqua (547), 4/20/14.
Scaled data, Aqua (547), 4/20/14.
Raw data, Aqua (547), 1/13/14.
Scaled data, Aqua (547), 1/13/14.
Scaled data, Aqua (547), 1/13/14.
Scaled data, Aqua (527), 6/7/09.
Scaled data, Aqua (527), 9/1/09.
Aqua (527) < 80, 9/1/09.

## Slide 13: Winter time snapshots (Aqua/Cloud)

## Slide 14: Results (Aqua)
If (5) and (7) < 20, count (4)
Chart: Days since 11/1/13
Chart: Days since 11/1/13
Ice start/end
Jam warning
Jam
Statistics | 
Mean | 6163
SD | 7630

## Slide 15: Concluding remarks
Relationship between temperature and ice quantity as expected
Cloud presence is a problem
  Retrieval despite cloud may help
  CM has some problems over river
Next steps
  Improve mask quality
    classify, i.e. max likelihood
  Retrieval despite cloud
    Histogram informed threshold?
  Generate NDSI, Ice Age
  Merge Aqua/Terra data
  Jam modeling
  Transfer to AK

## Slide 16: References
Vermote, E.F., Kotchenova, S.Y., 2008. MOD09 (Surface Reflectence) User’s Guide. http://modis-sr.ltdri.org/products/MOD09_UserGuide_v1_2.pdf
CRREL Ice Jam Database. http://icejams.crrel.usace.army.mil/
Chaouch, N., et al. "An automated algorithm for river ice monitoring over the Susquehanna River using the MODIS data." Hydrological Processes 28.1 (2012): 62-73.